## Slide 1: Introduction to Audio

## Slide 2: What is Audio?
Audio refers to sound that is recorded, transmitted, or reproduced.
It includes natural sounds, music, speech, and artificially generated signals.
Audio is represented as analog or digital signals.

## Slide 3: Analog vs Digital Audio
Analog Audio:
Continuous waveforms that closely mimic natural sound.
Captures and stores sound as electrical signals or mechanical imprints.
Examples: Vinyl records, cassette tapes, radio transmissions.
Digital Audio:
Sound is converted into discrete numerical values (samples) at specific intervals.
Allows for compression, editing, and transmission without degradation.
Examples: CDs, MP3s, streaming services like Spotify & YouTube Music.

## Slide 4: Properties of Sound
Frequency (Hz) – Determines pitch.
Amplitude – Determines loudness.
Timbre – Defines the quality of sound.
Speed – Depends on the medium of travel.

## Slide 5: How Audio is digitized?
Sample Rate:
The sample rate refers to how many times an audio signal is measured (sampled) per second .
44.1kHz Standard for CDs, used in most music.
48kHz  Used in professional audio and video production.
Bit Depth:
Determines the resolution of each sample, affecting audio quality and dynamic range.
16-bit CD quality (~96 dB dynamic range)
24-bit Studio quality (~144 dB dynamic range)
32-bit  Extreme high-fidelity (used in some professional recording)
Channels (Mono, Stereo, Surround):
Mono  Single channel, same sound in both ears (e.g., old radios, phone calls).
Stereo  Two channels (left & right), creating a spatial effect (used in music & films)
Sorround  Multiple channels (5.1, 7.1) for immersive 3D sound (home theaters, gaming).
Audio Data Size = Sample Rate x Bit Depth x Channels x Duration

## Slide 6: Common Audio Formats
MP3 – Lossy, Compressed, widely used.
WAV – Lossless, Uncompressed, high quality.
FLAC – Lossless, used for high-fidelity audio.
AAC – Used in streaming services.

## Slide 7: What is ALSA?
Advanced Linux Sound Architecture(ALSA) is a framework in the Linux kernel for managing the audio devices.
It provides low-level hardware access for sound cards and audio interfaces
Supports Audio Playback and Recording
Used by higher-level sound services like PulseAudio and Jack
Common Utilities are aplay, arecord, alsamixer

## Slide 8: Common ALSA Commands
aplay -l
It lists no.of playback devices
arecord –l
It lists no.of recording devices
alsamixer
It Adjusts volume settings
amixer
Command line mixer control

## Slide 9: Applications of Audio Technology
• Music production and playback
• Communication (phone, VoIP, radio)
• Film and television soundtracks
• Speech recognition (AI assistants)
• Medical applications (hearing aids)

## Slide 10: AUDIO TESTING
For testing audio, we used python automation
Functionalities
  Board support audio or not
  Mic and speakers available or not
  ALSA framework present or not
  Bitrates
  Codecs
  Recording and Playback

## Slide 11
While writing python script for audio we need import modules like
  os, re, subprocess, alsaaudio,time
Import os: The os module provides functions for interacting with the operating system.
  You can use it to handle file paths, environment variables, process management, and system commands.
Import re:The re module provides support for regular expressions (regex), which are used for pattern matching in strings.
Import subprocess: The subprocess module allows you to run system commands from Python scripts and capture their output.
Import time: The time module provides functions to work with time-based operations, such as delays and timestamps.